## Slide 1: Development of Optimal Ligament Wrapping Algorithm
Michael Vignos
ME 748
May 9th, 2016

## Slide 2: Musculoskeletal Multi-Body Modeling
Motion Capture Data
Muscle Forces
Ligament Forces
Cartilage Pressure

## Slide 3: Ligaments
Ligaments in musculoskeletal model
Human knee ligaments

## Slide 4: Shortcomings of Wrap Objects
Rapid Model Generation
Placing wrap objects in these models is infeasible
Wrap Object Limitations
Non-physiological approximation
Time consuming to place
Can sometimes give poor results

## Slide 5: Objective
To develop an efficient optimization routine to compute the wrapping of a ligament around two bones

## Slide 6: Optimization Problem
Objective:
Minimize the ligament length
Optimization Parameters:
Three-dimensional location of nodes on the ligament path
Constraint:
Nodes must lie on the surface of the bones
Additional Requirements:
Optimization needs to be fast
Ligament path needs to be smooth
(xi, yi, zi)
Femur Attachment Point
Tibia Attachment Point

## Slide 7: Optimization Approaches
Four optimization approaches
  Two unconstrained
  Two constrained
Optimization speed improved by providing analytical solution of gradient for objective function and constraints

## Slide 8: Method 1
П = potential energy of spring system
3D location for each node
N = total number of springs (Node-to-node AND bone-to-node)
, for all springs
fminunc
Femur
Tibia
= spring
= free node
= fixed node

## Slide 9: Signed Distance Field
Compute signed distance between a point and a closed surface
  + distance = outside surface
  - distance = inside surface
Tri-cubic interpolation to compute distance between field points
Significantly faster than searching for nearest point
Code provided by: G. Elisabeta Marai, Department of Computer Science, Brown University

## Slide 10: Gradient of Signed Distance Field
Used central finite difference to compute gradient at each field point
Tri-cubic interpolation to compute gradient for points that fall between field points

## Slide 11: Method 2
П = potential energy of spring system
penalty term based on distances of node from bone
3D location for each node
N = number of node-to-node springs
node-to-node spring stiffness
, for all springs
M = number of free nodes (N – 1)
“bone-to-node spring stiffness” (penalty term constant)
signed distance between node and bone
fminunc
Femur
Tibia
d1
d2
d3
d4
d5
= spring
= free node
= fixed node
= distance between node and bone
Advantage over method 1: Does not require all nodes to stay “attached” to bones

## Slide 12: Method 3
= distance between two nodes
3D location for each node
M number of free nodes
signed distance from a node to the bone surface
fmincon
= free node
= fixed node
Femur
Tibia
d1
D1
d5
D6
Advantage over method 2: Converges to a “good” solution faster due to analytical solution for gradient of constraints

## Slide 13: Method 4
П = potential energy of spring system
3D location for each node
N number of springs
node-to-node spring stiffness
, for all springs
signed distance from a node to the bone surface
M = number of free nodes (N – 1)
fmincon
Femur
Tibia
d1
= spring
= free node
= fixed node
d5
Advantage over method 3: Analytical solution for gradient of objective function and constraints

## Slide 14: Visual Accuracy Results
Solutions for the same convergence criteria
Method 1
Method 2
Method 3
Method 4

## Slide 15: Speed Results
Varied objective function tolerance to reduce convergence time
Method 1
Method 2
Method 3
Method 4
= tolerance needed for visually acceptable solution

## Slide 16: Best Method
П = potential energy of spring system
3D location for each node
N number of springs
node-to-node spring stiffness
, for all springs
signed distance from a node to the bone surface
M = number of free nodes (N – 1)
fmincon
Femur
Tibia
d1
= spring
= free node
= fixed node
d5

## Slide 17: Brief Sensitivity Analysis
Only for method 4 (best method)
Performed sensitivity analysis to understand how to improve convergence speed while maintaining accuracy
  Spring stiffness
  Number of nodes
  Initial guess

## Slide 18: Sensitivity to Initial Guess
Tested two initial guesses
Shows that using the solution at the previous time step of a simulation as the initial guess improves convergence
Convergence Time = 0.051 sec
Convergence Time = 0.12 sec

## Slide 19: Conclusions
Utilized optimization techniques discussed in class to implement an efficient ligament wrapping routine
Primary speed-ups:
  Implementing analytical solutions for gradients
  Good initial guess
Benchmark against wrap objects to assess accuracy and speed
Optimization seems fast enough to implement in simulation framework

## Slide 20: Development of Optimal Ligament Wrapping Algorithm
Michael Vignos
ME 748
May 9th, 2016

## Slide 21: Sensitivity to spring stiffness
Varied stiffness of springs between 0.01 and 100 N/mm
k = 0.01 N/mm
k = 0.1 N/mm
k = 0.5 N/mm
= tolerance needed for visually acceptable solution

## Slide 22: Sensitivity to number of nodes
Varied number of nodes between 5 and 30
= tolerance needed for visually acceptable solution
15 Nodes
10 Nodes
5 Nodes